## Slide 1: IEEE 802.15.4 Wireless Sensor Network
Yao-Tung Tsou

## Slide 2: IEEE 802.15.4 Applications Space
Home Networking
Automotive Networks
Industrial Networks
Interactive Toys
Remote Metering

## Slide 3: Some needs in the sensor networks
Sink node
Gateway
Core network
e.g. Internet
End-user
Computer services
Gateway
The networks typically run Low Power Devices
Consist of one or more sensors, could be different type of sensors
Use wireless communication protocols such as IEEE 802.15.4
Operate at 2.4 GHz and 250KB/s data rates
Sensor node

## Slide 4: 802.15.4 General Characteristics
Data rates of 250 kb/s, 40 kb/s and 20 kb/s.
Star or Peer-to-Peer operation.
Support for low latency devices.
Fully hand-shaked protocol for transfer reliability.
Low power consumption.
Frequency Bands of Operation
  16 channels in the 2.4GHz ISM* band
  10 channels in the 915MHz ISM band
  1 channel in the European 868MHz band.

## Slide 5: 802.15.4 / ZigBee Architecture
IEEE 802.15.4 MAC
Applications
IEEE 802.15.4
2400 MHz
PHY
IEEE 802.15.4
868/915 MHz
PHY
ZigBee
Packet generation
Packet reception
Data transparency
Power Management

## Slide 6: IEEE 802.15.4 PHY Overview Operating Frequency Bands
868MHz / 915MHz
PHY
2.4 GHz
868.3 MHz
Channel 0
Channels 1-10
Channels 11-26
2.4835 GHz
928 MHz
902 MHz
5 MHz
2 MHz
2.4 GHz
PHY

## Slide 7: IEEE 802.15.4 PHY Overview Packet Structure
Preamble
Start of
Packet
Delimiter
PHY
Header
PHY Service
Data Unit (PSDU)
PHY Packet Fields
Preamble (32 bits) – synchronization
Start of Packet Delimiter (8 bits)
PHY Header (8 bits) – PSDU length
PSDU (0 to 1016 bits) – Data field
6 Octets
0-127 Octets

## Slide 8: 802.15.4 Architecture
IEEE 802.15.4 MAC
Applications
IEEE 802.15.4
2400 MHz
PHY
IEEE 802.15.4
868/915 MHz
PHY
Channel acquisition
Contention mgt
NIC address
Error Correction
ZigBee

## Slide 9: IEEE 802.15.4 MAC Overview Design Drivers
Extremely low cost
Ease of implementation
Reliable data transfer
Short range operation
Very low power consumption
Simple but flexible protocol

## Slide 10: IEEE 802.15.4 MAC Overview Typical Network Topologies

## Slide 11: IEEE 802.15.4 MAC Overview Device Classes
Full function device (FFD)
  Any topology
  Network coordinator capable
  Talks to any other device
Reduced function device (RFD)
  Limited to star topology
  Cannot become a network coordinator
  Talks only to a network coordinator
  Very simple implementation

## Slide 12: IEEE 802.15.4 MAC Overview Star Topology
Full function device
Reduced function device
Communications flow
Master/slave
PAN
Coordinator

## Slide 13: IEEE 802.15.4 MAC Overview Peer-Peer Topology
Full function device
Communications flow
Point to point
Cluster tree

## Slide 14: IEEE 802.15.4 MAC Overview Combined Topology
Full function device
Reduced function device
Communications flow
Clustered stars - for example,
cluster nodes exist between rooms
of a hotel and each room has a
star network for control.

## Slide 15: IEEE 802.15.4 MAC Overview General Frame Structure

## Slide 16: IEEE 802.15.4 MAC Overview Traffic Types
Periodic data
  Application defined rate (e.g. sensors)
Intermittent data
  Application/external stimulus defined rate (e.g. light switch)
Repetitive low latency data
  Allocation of time slots (e.g. mouse)

## Slide 17: 802.15.4 Architecture
IEEE 802.15.4 MAC
Applications
IEEE 802.15.4
2400 MHz
PHY
IEEE 802.15.4
868/915 MHz
PHY
Network Routing
Address translation
Packet Segmentation
Profiles
ZigBee

## Slide 18: ZigBee Stack Architecture

## Slide 19: Typical ZigBee-Enabled Device Design
Typical design consist of RF IC and 8-bit microprocessor with peripherals connected to an application sensor or actuators

## Slide 20: Wireless Technology Comparison Chart

## Slide 21: 802.15.4/ZigBee Products
Control for Home Automation System
http://www.control4.com/products/components/complete.htm
Eaton Home HeartBeat monitoring system
www.homeheartbeat.com
Chip Sets
Ember, http://www.ember.com/index.html
ChipCon, http://www.chipcon.com
Freescale, http://www.freescale.com
Software, Development Kits
AirBee, http://www.airbeewireless.com/products.php
Software Technologies Group, http://www.stg.com/wireless/

## Slide 22: Motorola Activity
Implementation of 802.15.4 & ZigBee
Aimed at enterprises
  Asset Tracking
  Security
  Public Safety
Range: 10m
Transmission interval: ~ 4 minutes
Nodes move, Controller does not
Battery life: 1 week to several years (nodes with 2 AA batteries)
Interfaces: machine-only

## Slide 23: Sensor Platforms
  Sensor node/Mote: Small cache, low-speed CPU, wireless interface for transmission, battery, possibly with location information
  Sink node/Gateway: gather data from sensor nodes and forward gathered data to end-users.
  UC Berkeley, Smart Dust

## Slide 24: Sensor Platforms
Popular Sensor Platforms
  NTU
    Simple node / Super node / Taroko
  NTHU
    Octopus II / Octopus X
  NCTU
    Eco node
  UC Berkeley
    Tmote Sky
  M. Banzi et. al.
    Arduino
  Raspberry Pi Foundation
    Raspberry Pi

## Slide 25
Xbee / Xbee Pro

## Slide 26: XBee/XBee ‐ PRO RF Modules
The XBee and XBee-PRO RF Modules were engineered to meet IEEE 802.15.4 standards and support the unique needs of low-cost, low-power wireless sensor networks.
The modules require minimal power and provide reliable delivery of data between devices.
The modules operate within the ISM 2.4 GHz frequency band and are pin-for-pin compatible with each other.

## Slide 27: Long Range Data Integrity
XBee
• Indoor/Urban: up to 100’ (30 m)
• Outdoor line-of-sight: up to 300’ (90 m)
• Transmit Power: 1 mW (0 dBm)
• Receiver Sensitivity: -92 dBm
XBee-PRO
• Indoor/Urban: up to 300’ (90 m), 200' (60 m) for International variant
• Outdoor line-of-sight: up to 1 mile (1600 m), 2500' (750 m) for International variant
• Transmit Power: 63mW (18dBm), 10mW (10dBm) for International variant
• Receiver Sensitivity: -100 dBm
RF Data Rate: 250,000 bps

## Slide 28: Low Power
XBee
• TX Peak Current: 45 mA (@3.3 V)
• RX Current: 50 mA (@3.3 V)
• Power-down Current: < 10 μA
XBee-PRO
• TX Peak Current: 250mA (150mA for international variant)
• TX Peak Current (RPSMA module only): 340mA (180mA for international variant
• RX Current: 55 mA (@3.3 V)
• Power-down Current: < 10 μA

## Slide 29
Xbee / Xbee Pro

## Slide 30: XBee
This is the new 2.4GHz XBee module from Digi. These modules take the 802.15.4 stack (the basis for Zigbee) and wrap it into a simple to use serial command set.
  250kbps Max data rate
  400ft (120m) range
  6 10-bit ADC input pins and 8 digital IO pins
  128-bit encryption
  Local or over-air configuration

## Slide 31: XBee/XBee ‐ PRO RF Modules
The XBee and XBee-PRO RF Modules were engineered to meet IEEE 802.15.4 standards and support the unique needs of low-cost, low-power wireless sensor networks.
The modules require minimal power and provide reliable delivery of data between devices.
The modules operate within the ISM 2.4 GHz frequency band and are pin-for-pin compatible with each other.

## Slide 32: Long Range Data Integrity
XBee
• Indoor/Urban: up to 30 m
• Outdoor line-of-sight: up to 90 m
• Transmit Power: 1 mW (0 dBm)
• Receiver Sensitivity: -92 dBm
XBee-PRO
• Indoor/Urban: up to 90 m
• Outdoor line-of-sight: up to 1600 m
• Transmit Power: 63mW (18dBm)
• Receiver Sensitivity: -100 dBm
RF Data Rate: 250,000 bps

## Slide 33: Low Power
XBee
• TX Peak Current: 45 mA (@3.3 V)
• RX Current: 50 mA (@3.3 V)
• Power-down Current: < 10 μA
XBee-PRO
• TX Peak Current: 250mA
• RX Current: 55 mA (@3.3 V)
• Power-down Current: < 10 μA

## Slide 34: ADC and I/O line support
Analog-to-digital conversion, Digital I/O Line Passing

## Slide 35: Easy-to-Use
No configuration necessary for out-of- box RF communications
Free X-CTU Software (Testing and configuration software)
AT and API Command Modes for configuring module parameters
Extensive command set

## Slide 36: AT vs API
In AT Command mode(Transparent Mode) , everything got in RX of XBee will be sent out via antenna , the incoming data from antenna will go to TX. But in API Mode , it won't send out anything until it received the correct form of commands from serial interface.

## Slide 37: API
The API allows the programmer the ability to:
  Change parameters without entering command mode
  View RSSI and source address on a packet by packet basis
  Receive packet delivery confirmation on every transmitted packet

## Slide 38: API

## Slide 39: Specifications

## Slide 40: Specifications

## Slide 41: Mechanical Drawings

## Slide 42: Pin Signals

## Slide 43: RF Module Operation
Serial Communications
  The XBee/XBee-PRO RF Modules interface to a host device through a logic-level asynchronous serial port.
  Through its serial port, the module can communicate with any logic and voltage compatible UART.
  Or through a level translator to any serial device (For example: Through a RS-232 or USB interface board).

## Slide 44: UART Data Flow

## Slide 45: Serial Data
Data enters the module UART through the DI pin (pin 3) as an asynchronous serial signal.
  The signal should idle high when no data is being transmitted.
Each data byte consists of a start bit (low), 8 data bits (least significant bit first) and a stop bit (high).
  The following figure illustrates the serial bit pattern of data passing through the module.

## Slide 46: Serial Data
Serial communications depend on the two UARTs (the microcontroller's and the RF module's) to be configured with compatible settings (baud rate, parity, start bits, stop bits, data bits).
The UART baud rate and parity settings on the XBee module can be configured with the BD and SB commands, respectively.

## Slide 47: Transparent Operation
By default, XBee/XBee-PRO RF Modules operate in Transparent Mode.
  When operating in this mode, the modules act as a serial line replacement
    all UART data received through the DI pin is queued up for RF transmission. When RF data is received, the data is sent out the DO pin.

## Slide 48: Serial-to-RF Packetization
Data is buffered in the DI buffer until one of the following causes the data to be packetized and transmitted:
  No serial characters are received for the amount of time determined by the RO (Packetization Timeout) parameter.
    If RO = 0, packetization begins when a character is received.
  The maximum number of characters that will fit in an RF packet (100) is received.
  The Command Mode Sequence (GT + CC + CT) is received.
    Any character buffered in the DI buffer before the sequence is transmitted

## Slide 49: Serial-to-RF Packetization
If the module cannot immediately transmit (for instance, if it is already receiving RF data), the serial data is stored in the DI Buffer. The data is packetized and sent at any RO timeout or when 100 bytes (maximum packet size) are received.
If the DI buffer becomes full, hardware or software flow control must be implemented in order to prevent overflow (loss of data between the host and module).

## Slide 50: API Operation
API (Application Programming Interface) Operation is an alternative to the default Transparent Operation.
  The frame-based API extends the level to which a host application can interact with the networking capabilities of the module.
  When in API mode, all data entering and leaving the module is contained in frames that define operations or events within the module.

## Slide 51: API Operation
Transmit Data Frames (received through the DI pin (pin 3)) include:
  RF Transmit Data Frame
  Command Frame (equivalent to AT commands)
Receive Data Frames (sent out the DO pin (pin 2)) include:
  RF-received data frame
  Command response
  Event notifications such as reset, associate, disassociate, etc.

## Slide 52: API Operation
The API provides alternative means of configuring modules and routing data at the host application layer.
A host application can send data frames to the module that contain address and payload information instead of using command mode to modify addresses.
The module will send data frames to the application containing status packets; as well as source, RSSI and payload information from received data packets.

## Slide 53: API Operation
The API operation option facilitates many operations such as the examples cited below:
  -> Transmitting data to multiple destinations without entering Command Mode
  -> Receive success/failure status of each transmitted RF packet
  -> Identify the source address of each received packet

## Slide 54: Flow Control

## Slide 55
Implementation

## Slide 56: Introduction
This basic chat tutorial shows you how to get wireless text chat going between two computers using Digi’s XBee 802.15.4 Wireless Modules (formerly called XBee Series 2). Using a serial connection from your computer, the text you type to one XBee will be wirelessly transmitted to the other XBee, which will send the text via serial to your other computer.

## Slide 57: Assemble the Parts
2 XBee 802.15.4 Radios (Series 2)
2 XBee usb adapter
2 Two computers, each running a serial terminal program, or one computer running two different serial terminal programs.

## Slide 58: Step 1: Download X-CTU Software
The X-CTU software is free to download and provides a simple interface to configure and update your XBee transceivers. With this software firmware updates are a breeze and configuration is simple. The software can be downloaded from Digi's website found:
  http://www.digi.com/products/xbee-rf-solutions/xctu-software/xctu

## Slide 59: Step 2: Connection
Adapter allows for connection through usb or serial to your computer.
Use X-CTU to configure your Xbee.

## Slide 60: Step 3: Configure 1st XBee as a coordinator
When opening the X-CTU software you should see a window like that shown. After selecting the proper COM port click the Test/Query button.

## Slide 61: Step 3: Configure 1st XBee as a coordinator
After selecting the Test/Query button, you should see a dialogue box like the one below. You will want to record the serial number shown as you will need it in a couple minutes.

## Slide 62: Step 3: Configure 1st XBee as a coordinator
After recording the serial number you can click OK. Next, select the Modem Configuration tab at the top of the window. Once here, select the read button. This will bring up the current configuration for the connected XBee and will be similar to the following:

## Slide 63: Step 3: Configure 1st XBee as a coordinator
Once here, you want to select Zigbee Coordinator AT in the function set drop down menu.

## Slide 64: Step 3: Configure 1st XBee as a coordinator
After selecting the coordinator function set, you will need to set the PAN ID. This can be any four digit number and allows the XBees to distinguish between modules in their network and those from other networks. Once you have added the wanted PAN ID click the "Write" button. This will update and configure the XBee. Once this is done you can disconnect the XBee and plug in the second XBee.

## Slide 65: Step 4: Configure 2nd XBee as Router
To configure the 2nd XBee, you will follow the same process as for the coordinator with one difference. In the PC settings tab, again, click the "Test/Query" button and record the serial number. Then in the Modem configuration tab, click the read button to load the current configuration of the XBee and set the PAN ID to the same ID used for the coordinator. The only change will be the function set you choose. For the second XBee we will set this as Zigbee Router AT.

## Slide 66: Step 4: Configure 2nd XBee as Router
After setting the PAN ID and the function set for the router you will put the recorded serial numbers to use. Enter the first 6 digits of the coordinators serial number into the Destination Address High field and the rest of the serial number into the Destination Address Low field. Then select the "Write" button to update the configuration settings for the router. Once this is done updating you can disconnect the router and reconnect the coordinator to the computer.

## Slide 67: Step 4: Configure 2nd XBee as Router
After re-connecting the coordinator to the computer. You will again go into the Modem Configuration tab and click the read button. You will then want to set the Destination Address to the serial number of the Router XBee in the same manner as you just did for the Router.
Once done you will again click the write button to update the coordinator XBee settings. After the write process is complete you are ready to use your XBees and communicate wirelessly!

## Slide 68: Step 5: Test the configuration
A simple test can be done to be sure the two XBees are communicating properly. You can connect either one of the XBees to the computer. Then, connect the second XBee to 3.3V power and connect the Dout and Din pins together. This will cause the XBee to automatically retransmit any data it receives.

## Slide 69: Step 5: Test the configuration
When you have both XBees connected go to the Terminal tab in the X-CTU window. Whatever you type in the terminal window will appear in blue font and whatever is received will appear in red font. If the XBees are configured correctly every character you type should be mirrored in red.

## Slide 70: Step 5: Test the configuration
When typing single characters, you should see a screen similar to the one above. To send strings of data you can assemble a data packet. To do this click the "Assemble Packet" button and type the wanted string into the box then click send data. This will send the entire packet before receiving the same packet back.

## Slide 71
Lab: Sending temperature data via XBee

## Slide 72: Sending temperature data via XBee
Connecting LM35 to Pi A and sending temperature data to Pi B through Xbee module
Setting one is coordinator and the other is endpoint/router

## Slide 73: Open serial port
“serial” module is required.
Open serial port
  serial.serial(‘/dev/ttyUSB0’, [baud rate])
Check ComPort
  object.isOpen()
  object.name

## Slide 74: Serial write and read
Serial write
  object.write([data])
Serial read
  object.readline()

## Slide 75: Using thread
Evaluating thread funtion
  “threading” module is required
  threading.Thread(target=[function name], args=(ser, ))

## Slide 76
End